## Slide 1
2026 WAC Summit
Donnie Brackett

## Slide 2: International Radioactive Material Acceptance Criteria

## Slide 3: International Radioactive Material Acceptance Criteria
WAG-502 International Radioactive Material Acceptance Guidelines
WAG-503 International Radioactive Metals Acceptance Guidelines

## Slide 4: International Radioactive Material Acceptance Criteria
IMPORT/EXPORT CONSIDERATIONS
If you wish to export radioactive material, you will need to comply with the exporting country’s regulations.
Since EnergySolutions can not dispose of any international radioactive material (processed or unprocessed), ES will not be required to obtain an import permit.
However, if any radioactive material (processed or unprocessed) is to be returned to the customer, ES will have to obtain an export permit.

## Slide 5: International Radioactive Material Acceptance Criteria
RESIDUAL WASTE
NRC Definition - Residual waste means low-level radioactive waste resulting from processing or decontamination activities that cannot be easily separated into distinct batches attributable to specific waste generators. This waste is attributable to the processor or decontamination facility, as applicable.
  Metal Melt – All slag from cutting and sizing metal, melting of the metal, PPE, floor sweepings, metal waste from grinding of blocks are considered secondary waste and are the responsibility of ES and are not returned to the customer.

## Slide 6: International Radioactive Material Acceptance Criteria
SECONDARY WASTE (continued)
  DAW Incineration – Hearth ash is returned to the customer. All other waste (secondary chamber ash, baghouse filters, PPE, etc.) are considered secondary waste and are the responsibility of ES and are not returned to the customer.
  Oil Incineration – this is injected into the secondary chamber and any ash from ash is considered secondary waste and are the responsibility of ES and are not returned to the customer.

## Slide 7: International Radioactive Material Acceptance Criteria
SECONDARY WASTE (continued)
  Liquid Processing – Liquids to be evaporated or incinerated are pumped into a feed tank that contains multiple customer liquids. Once liquid is pumped into the feed tank it loses its customer identity and is considered ES waste. Any residual solids or ash is considered as ES secondary waste and not returned to the customer.
  Compaction – Compacted material is returned to the customer. All other waste (PPE, sump liquids/sludges, etc.) are considered secondary waste and are the responsibility of ES and are not returned to the customer.

## Slide 8: International Radioactive Material Acceptance Criteria
Any waste defined below is prohibited from import without authorization of the US Environmental Protection Agency (USEPA) and the exporting country’s appropriate regulatory authority.
  Hazardous as defined in 40 CFR 261
  Off-specification used oil as defined in 40 CFR 279

## Slide 9: International Radioactive Material Acceptance Criteria

## Slide 10: International Radioactive Material Acceptance Criteria

## Slide 11: International Radioactive Material Acceptance Criteria
Metal Criteria
A. Radiation and Contamination Level of Metal for Recycle |  | 
Metal Type | Contact Dose Rate with Metal | Removable Contamination (Bq/cm2)1
Metal for Recycling through Melting | ≤ 200 µSv/hr | ≤8 β–γ ≤1 α
Lead for Casting | ≤ 50 µSv/hr | 0.1 α for Uranium and daughters, 0.08 α for transuranics and Thorium, and less than 4 β–γ
B. Radionuclide Concentration | 
Radionuclide concentration per package shall not exceed the following limits without prior evaluation and approval. | 
Metals for Recycle | Limiting Values
All Nuclides | ≤ 5000 Bq/gm
Co-60 | ≤ 40 Bq/gm
Cs-137 | ≤ 5000 Bq/gm
Ni-63 | ≤ 5000 Bq/gm
C-14 | ≤ 1000 Bq/gm
H-3 | ≤ 1000 Bq/gm
Sr-90 | ≤ 35 Bq/gm
Pu-241 | ≤ 800 Bq/gm
Total Transuranics (sum of Am-241, Pu-238. Pu-239. Cm-243. Cm-244) | ≤ 20 Bq/gm
Special Nuclear Material | ≤ 0.49 grams
Source Material | ≤ 0.49 kgs

## Slide 12: International Radioactive Material Acceptance Criteria
Other Radioactive Material Criteria
Other Waste Streams | Limiting Values
Total, all radionuclides with >5-yr half-lives except H-3 and C-14 | ≤ 11 kBq/cc
Total, H-3 and C-14 | ≤ 5 kBq/cc
I-125 | ≤ 3700 kBq/package
Other mixed fission and activation products, Z <84 | ≤ 200 kBq /cc
Tc-99 | ≤0.13 kBq/cc
Th-232 | ≤40 kBq/m3 or 1e-5 gm Th/cc of waste
U-238 as metal or oxide | ≤20 kBq/cc or 1.6E-3 g U/cc of waste
Depleted Uranium or Natural Uranium as metal or oxide | ≤ 120 kBq / m3 or 6e-6 gm U/cc of waste
Alpha for TRUs, Ac, Ra-226 and Th for processing. Packages shall be clearly marked for identification. | ≤ 3.7 Bq/g and less than 1% of activity
No shipment shall equal or exceed 10 CFR 110, Appendix P Category 2 quantities of radionuclides (Sum of Fractions Applies) | 
Special Nuclear Material | ≤ 0.49 grams
Source Material | ≤ 0.49 kgs

## Slide 13: International Radioactive Material Acceptance Criteria Contact Colin R. Austin President, International Group EnergySolutions Cell: +1 706 830 4959 caustin@energysolutions.com

## Slide 14: International Radioactive Material Acceptance Criteria Questions?